Roomba manual

Name : iRobot Roomba
Series : 530
Datasheet : http://irobot.lv/uploaded_files/File/iRobot_Roomba_500_Open_Interface_Spec.pdf

## Configuration Serial Port :
Baud: 115200 (défaut, possible pour l'arduino) or 19200 (si limité par micro-contrôlleur)
Data bits: 8
Parity: None
Stop bits: 1
Flow control: None

## Matching pin arduino → Roomba

M1- (Shield); _ => Câble BLANC (gros) : Alimentation Moteur pôle négatif ?
M1+ (Shield); _ => Câble BLANC (gros) : Alimentation Moteur pôle positif ?
GND (Shield); _ => Câble NOIR (gros) : Prise de terre Arduino ?
Vin (Shield); _ => Câble ROUGE (gros) : Alimentation Arduino pôle positif ?
GND (Shield); 6 ou 7 (GND) => Câble JAUNE-VERT : Prise de terre Arduino
5V (Shield); [Boussole] VCC => Câble ROUGE (petit) : Alimentation Compas Gyroscopique
GND (Shield); [Boussole] GND => Câble NOIR (petit) : Prise de terre Compas Gyroscopique
TX1 18 ; RXD => Câble MARRON (petit) : Output Arduino vers Input Roomba
RX1 19 ; TXD => Câble BLEU (petit) : Output Roomba vers Input Arduino
SDA 20; [Boussole] SDA => Câble BLANC (petit) : Bus I2C Data
SCL 21 ; [Boussole] SCL => Câble JAUNE (petit) : Bus I2C Clock

## Typical use case of the roomba :
1. Start Roomba with sequence : [128]
2. Roomba in Off mode after being started.
3. (Optional) [129][Baud Code] (voir doc technique pour Baud Code)
4. Change Roomba into Safe Mode : [131]
5. All the request you want to do
6. Power down Roomba : [133]

## Useful commands :

Seek Dock : [143]
Set Clock : [168][Day][Hour][Minute]

## Navigation commands:

- Drive : [137] [Velocity high byte] [Velocity low byte] [Radius high byte] [Radius low byte]
   • 4 bytes interpreted as two 16 bit signed values
• Velocity (-500 – 500 mm/s)
• Radius (-2000 – 2000 mm

- Drive Direct:	[145] [Right velocity high byte] [Right velocity low byte] [Left velocity high byte][Left velocity low byte]
• 4 bytes interpreted as two 16 bit signed values
• Right wheel velocity (-500 – 500 mm/s)
• Left wheel velocity (-500 – 500 mm/s)
## Sensors :
### Commands :
- sensor : [142] [Packet ID]
- Query List : [149][Number of Packets][Packet ID 1][Packet ID 2]...[Packet ID N]
- Stream : [148] [Number of packets] [Packet ID 1] [Packet ID 2] [Packet ID 3]
• Requested data sent every 15 ms, which is the rate Roomba uses to update data.
• Value returned in format : [19][N-bytes][Packet ID 1][Packet 1 data…][Packet ID 2][Packet 2 data…][Checksum]
• The checksum is a 1-byte value. It is the 8-bit complement of all of the bytes between the header and the checksum. That is, if you add all of the bytes after the checksum, and the checksum, the low byte of the result will be 0.

### Packet ID :

Most of the packets (numbers 7 – 58) contain the value of a single sensor or variable, which can be either 1 byte or 2 bytes. Two byte packets correspond to 16-bit values, sent high byte first. Some of the packets (0-6, 100-107) contain groups of the single-value packets. (See datasheet for more info)

- Wall Signal	Packet ID: 27	Data Bytes: 1, unsigned	Range: 0-1023.
- Cliff Left Signal	Packet ID: 28	Data Bytes: 1, unsigned	Range: 0-4095
- Cliff Front Left Signal	Packet ID: 29	Data Bytes: 1, unsigned	Range: 0-4095
- Cliff Front Right Signal	Packet ID: 30	Data Bytes: 1, unsigned	Range: 0-4095
 - Cliff Right Signal	Packet ID: 31	Data Bytes: 1, unsigned	Range: 0-4095
- Distance	Packet ID: 19	Data Bytes: 2, signed	Range: -32768 – 32767
- Angle	Packet ID: 20	Data Bytes: 2, signed	Range: -32768 – 32767
- Right Encoder Counts Packet ID: 43	Data Bytes 2, unsigned	Range: 0 - 65535
- Left Encoder Counts Packet ID: 44	Data Bytes 2, unsigned	Range: 0 - 65535
- Stasis	Packet ID: 58	Data Bytes: 1
The stasis caster sensor returns 1 when the robot is making forward progress and 0 when it is not. This always returns 0 when the robot is turning, driving backward, or not driving.
Range: 0 – 1